## Slide 1: HNSCC functional assay pipeline development
Nate Evans

## Slide 2: Panel Assay Data Naming Convention
Currently, renamed data is only stored locally. I’ll add a box folder in the future.
Deviation from the naming convention will result in failed processing.
HNSCC-Format Plate Maps; Each panel has meta data page and a inhibitor-name, inhibitor-concentration page for each plate.
lab_id=10004-norm=Blank490-plate_version_id=OHSU_HNSCC_derm002-note=NA

## Slide 3
Plate Mapping
Negative Controls Normalization
Photo spectrometer
Output
Plate Map
Floor Normalization
Within & Across Plate Inhibitor Averaging
Ceiling Normalization
Combination-Agents Normalization
Regression Fitting
Single agents
post-processing
Check ‘Blank490’
No within plate replicates on these panels [rev 001, 002]
Convert from matrix format to long data and merge plate map.
Represented combination-agent conc. as Euclidean distance.
(drg1_conc^2 + drg2_conc^2)^(0.5)
Cell Viability
Drug 1 conc.
Drug 2 conc.
Cell
viability
The zero value (positive control) of optical density is set by the p.spec software [blank490] but to interpret assay value as cell viability, we need to scale optical density by plate controls:
Cell_viab = opt_dens / avg_plt_control
[This sets PAC control value as cell viability of 1]
?
Set floor of zero; Currently, truncate negative values to zero.
Dan’s protocol uses a Negative assay value adjustment.
Each within-plate replicate is fit with linear regression and drugs with AUC differences > 1 are flagged (within_plate_repl_flag); Replicates are then averaged.
Each across-plate replicate is fit with linear regression and drugs with AUC differences > 0.75 are flagged (across_plate_repl_flag); Replicates are then averaged.
Apply ceiling of 1
(Dan’s protocol uses 100 – note for AUC threshold adjustments)
Probit Regression & 5th order polynomial regression. For each calculate:
AIC, BIC
Deviance
P value, z-statistic
AUC
Remove runs with:
[probit] AIC > 12
[probit] Deviance > 2
Flag runs where:
[probit] AIC < [poly reg] AIC

## Slide 4
CONTROLS
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE
DOSE
DOSE
DOSE
DOSE
DOSE
DOSE
DOSE
DRUG X
AUC
Log(dose)
% viability
AUC
Probability
SENSITIVE
RESISTANT
0.9
1.1
0.9
1.0
1.1
1.0
0.9
0.7
0.5
0.3
0.1
0.1
Notes: Patient should be BIOPSIES or LAB _ID , separate from clinical study…
Change tail colors to match aucs in next slide!!! And copy
Add numbers in the dose 1-7 wells and plot points on the dose response curve.
Explain AUC: fill in area under the curve

## Slide 5
AUC
Probability
SENSITIVE
RESISTANT
LOW AUC
(Sensitive)
% viability
Log(dose)
MID AUC
HIGH AUC
(Resistant)
Notes: In inhibition model: high auc – greater resistance, low auc – lower resistance
Change position

## Slide 6: Sensitivity Assignment
Observations are filtered based on QC metrics prior to assignment (Issue #14)
0.2, 0.8 quantile assignment (“Tails” are each 20% of full distribution)

## Slide 7: Documentation
All code and documentation is stored in a private github repo. (https://github.com/nathanieljevans/HNSCC_functional_data_pipeline)
Wiki Pages; Wet-lab protocols, DR_ViewerApp_Tutorial, etc.
Issues – Bug tracking, feature requests, etc
Data Dictionary

## Slide 8: Pipeline Testing
Doctesting [python]
Unit Testing: Using Data from the BeatAML (Sorafenib, n=851), run the HNSCC pipeline and compare output to BeatAML reported values.
    Compare AUC calculation, allow deviance due to minor fitting differences
    Compare Sensitivity Assignment, allow no deviance
Travis.CI, commit triggered & cloud hosted build testing.

## Slide 9: Pipeline Validation (power analysis)
Simulate data using `synthetic_doseresponse_generator` output. (https://github.com/nathanieljevans/synthetic_doseresponse_generator)
Compare HNSCC-pipeline AUC to synthetic AUC and vary noise/replicates

## Slide 10: Visualization and Results Interactions
Raw output is saved as: ./output/HNSCC_all_functional_data.csv
Future filtering script will save filtered final data to separate file (Issue #16)
DR_ViewerApp
  Feedback welcome!
  Host via R cloud? Data-accessibility issues.

## Slide 11: DR_ViewerApp

## Slide 12: Processing Time & Parallelization
[20/21] - Total time elapsed: 0:25:10.298157
    ~75 sec / panel
Processing can be parallelize to the panel-level
  If our available nodes are greater than the number of panels to process: parallelization will reduce time complexity to O(c) ~ 75s
  Otherwise, O(n)

## Slide 13: Probit Fitting Convergence
Perfect separation occurs when all [or most; Issue #15] of the cell viability values are identical.
  If all are identical I fit with the max auc value, 1*log_conc_range
  If not all are identical [issue #15], I fit with linear regression – logistic or rectangle integration might be more intelligent here.

## Slide 14: TODO & Questions
Testing / Validation dev.
Drug synergies
Tyner plate-maps
Batch Effect Analysis
Report Requests?