## Slide 1: HNSCC functional assay pipeline development
Nate Evans

## Slide 2
Plate Mapping
Negative Controls Normalization
Photo spectrometer
Output
Plate Map
Floor Normalization
Within & Across Plate Inhibitor Averaging
Ceiling Normalization
Combination-Agents Normalization
Regression Fitting
Single agents
post-processing
Check ‘Blank490’
No within plate replicates on these panels [rev 001, 002]
Convert from matrix format to long data and merge plate map.
Represented combination-agent conc. as Euclidean distance.
The zero value (positive control) of optical density is set by the p.spec software [blank490] but to interpret assay value as cell viability, we need to scale optical density by plate controls:
Cell_viab = opt_dens / avg_plt_control
[This sets PAC control value as cell viability of 1]
Set floor of zero
QC: Negative assay value adjustment ?
Within-plate replicates are fit with linear regression and drugs with AUC differences > 1 are removed. Remaining are averaged.
Across-plate replicates are fit with linear regression and AUC differences > 0.75 are removed. Remaining are averaged.
Apply ceiling of 1
(Dan’s protocol uses 100 – note for AUC threshold adjustments)
Probit Regression & 5th order polynomial regression. For each calculate:
AIC, BIC
Deviance
P value, z-statistic
AUC
Remove runs with:
[probit] AIC > 12
[probit] Deviance > 2
Flag runs where:
[probit] AIC < [poly reg] AIC
Step Description:

## Slide 3
Regression Fitting
[Probit_calc.py]
post-processing
[name – not in dev yet]
Regression Fitting
[Probit_calc.py]
post-processing
[name – not in dev yet]
Regression Fitting
[Probit_calc.py]
post-processing
[name – not in dev yet]
Regression Fitting
[Probit_calc.py]
post-processing
[name – not in dev yet]
Panel 1
Panel 2
Panel 3
Panel n
Merge data
Filter Data
EDA / Batch Effects Search
Batch Effect Correction
[If necessary]
Assign Sensitivity Labels

## Slide 4: Combination-agent concentration space fit
For combination-agent assays, we have to choose a plane to fit our probit along and we really only have one good choice.
Drug 1 concentration
Drug 2 concentration
Cell
viability
(drg1_conc^2 + drg2_conc^2)^(0.5)
Cell viab

## Slide 5: Probit Fitting Convergence
Perfect separation occurs when all [or most] of the cell viability values are identical.
  If all are identical I just fit with the max auc value
  If not all are identical, I fit with linear regression.

## Slide 6: Processing Time & Parrallelization
[20/21] - Total time elapsed: 0:25:10.298157
    ~75 sec / panel
Processing can parallelize to panel granularity
  assuming available_threads > num_panels, parallelization will reduce time complexity to O(c)
  Otherwise, O(n)

## Slide 7: Overview
Number of HNSCC patients: 11 HNSCC patients [7/20]
Plate map versions
  Plates 1-3 (rev 001), Plates 1-6 (rev 002) <- combinatorial
  Tyner panels – still need to be re-worked into HNSCC format
  +1 assay with 7… require additional work
  Excel files with pages: meta, concentration_<num>, inhibitor_<num>
Naming convention
  Unique ID for each assay? Or we need to distinguish replicates
  Date of assay?
  MTS sitting time?
  lab_id=XXXXX-norm=XXX-plate_version_id=XXXX

## Slide 8: Plate Map Revisions
Drug Names, there are some inconsistencies – need to define clear nomenclature to avoid redundancy.
  I can provide a list of all used names, if someone can review and choose the right names.
  Alternatively, if there is a list of acceptable drug names, I can do it myself.
I’d like a review of my concentration mapping [request]
  Ashley volunteered to review, but a second pair of eyes would be useful as well.

## Slide 9: Data output documentation issues
There are a number of assays that are labeled as having been normalized by positive controls (labeled as “blank490”), however, the output file shows discrepancies that indicate it was not.
[lab_id=10308,notes=NA]
[lab_id=10309,notes=matched normal 10308]
*these two assay outputs don’t have a 26th column, which usually says “blank490” in each row.

## Slide 10: Standing Questions
Blank 490, how is this normalization done?
Scope of documentation?
  Code version control – github repo?
  Biocompute object
  R/Doxygen
Scope of testing?
  Doc-testing / unit-testing
Language Preference? Currently using mix of python, R, bash
Dockerize environment?

## Slide 11: Verification
Run beatAML data and compare to values
Unit testing
Doc testing

## Slide 12: Overview: Map data
$ python ./python/HNSCC_plate_data_mapper.py ./plate_maps ./data
Unique inhibitor names
Functional Data: position, lab_id -> concentration, inhibitor (long format)

## Slide 13
Functional Assay
Photo spectrometer
Output
Dose, inhibitor -Optical Density Mapping
Plate Map
EDA / Batch-Effect Search
Curve fitting / AUC calculation
[Traditional]
BDR sensitivity designation
[evans]
Normalization & QC [traditional]
Atypical classifier
[evans]
output
Inhibitor level EDA