## Slide 1: HNSCC functional assay pipeline development
Nate Evans

## Slide 2
Functional Assay
Photo spectrometer
Output
Dose, inhibitor -Optical Density Mapping
Plate Map
EDA / Batch-Effect Search
Curve fitting / AUC calculation
[Traditional]
BDR sensitivity designation
[evans]
Normalization & QC [traditional]
Atypical classifier
[evans]
output
Inhibitor level EDA

## Slide 3
The zero value (positive control) of optical density is set by the p.spec software [blank490] but to interpret this value as cell viability, we need to scale optical density by plate controls….eg
Cell_viab = opt_dens / avg_plt_control
Convert from matrix format to long data and merge plate map. Critical output features:
[conc, optical_density, lab_id, inhibitor]
Plate Mapping
[HNSCC_plate_data_mapper.py]
Normalization (1)
[name – not in dev yet]
Photo spectrometer
Output
Plate Map
Single-agent / Combination Split
[name – not in dev yet]
A ceiling and floor must be set to constrain cell viability within [0,1].
Normalization
(2)
[name – not in dev yet]
If we have replicates, then they are averaged.
Normalization
(3)
[name – not in dev yet]
??? Check Dan Bottomly’s documentation ??? I believe this step drops data when replicate_auc – avg_replacate_auc > some_value
Quality Control
[name – not in dev yet]
Combination-Agents Normalization
[name – not in dev yet]
Concentrations have to be represented as euclidean distances in concentration space to provide accurate plate to fit along.
Probit Fit & Overfitting QC
[name – not in dev yet]
Single agent

## Slide 4: Overview
Number of HNSCC patients: 11 HNSCC patients [7/20]
Plate map versions
  Plates 1-3 (rev 001), Plates 1-6 (rev 002) <- combinatorial
  Tyner panels – still need to be re-worked into HNSCC format
  +1 assay with 7… require additional work
  Excel files with pages: meta, concentration_<num>, inhibitor_<num>
Naming convention
  Unique ID for each assay? Or we need to distinguish replicates
  Date of assay?
  MTS sitting time?
  lab_id=XXXXX-norm=XXX-plate_version_id=XXXX

## Slide 5: Plate Map Revisions
Drug Names, there are some inconsistencies – need to define clear nomenclature to avoid redundancy.
  I can provide a list of all used names, if someone can review and choose the right names.
  Alternatively, if there is a list of acceptable drug names, I can do it myself.
I’d like a review of my concentration mapping [request]
  Ashley volunteered to review, but a second pair of eyes would be useful as well.

## Slide 6: Data output documentation issues
There are a number of assays that are labeled as having been normalized by positive controls (labeled as “blank490”), however, the output file shows discrepancies that indicate it was not.
[lab_id=10308,notes=NA]
[lab_id=10309,notes=matched normal 10308]
*these two assay outputs don’t have a 26th column, which usually says “blank490” in each row.

## Slide 7: Standing Questions
Blank 490, how is this normalization done?
Scope of documentation?
  Code version control – github repo?
  Biocompute object
  R/Doxygen
Scope of testing?
  Doc-testing / unit-testing
Language Preference? Currently using mix of python, R, bash
Dockerize environment?

## Slide 8: Overview: Map data
$ python ./python/HNSCC_plate_data_mapper.py ./plate_maps ./data
Unique inhibitor names
Functional Data: position, lab_id -> concentration, inhibitor (long format)